## Slide 1: Microgravity Washing Machine Summer 2021 Washing Machine Design Iteration
Design & Presentation by Thomas Rohmann

## Slide 2: Table of Contents
Background Information
Problem Statement 3
Goal of Design
Criteria and Constraints
The Basic Wash Cycle
Scope of Design
Design
Basic Functional Overview
Secondary Components Essential to Design Function
Additional Components and Functions
Determining Materials to be used
Project Testing
Microgravity compatibility
Wash Effectiveness
Clothing Wear Over Time
Additional Info
Unexplored Design Space
Environmental Challenges & Reasoning for Criteria & Constraints

## Slide 3: Problem Statement
Traditional washing machines are not designed to work in microgravity environments or accommodate for the scarcity of resources on a spaceship. Because of this, there is currently no way of washing clothing in space.
Current day workarounds to this problem such as getting resupplies and packing absorbent amounts of clothing do not scale well with prolonged and ever distant space flights. Because of this, with no feasible alternative to washing clothing, This is a huge barrier to space exploration and long duration space flights.

## Slide 4: The goal of this machine is to wash one clothing item in an automated process
What this means is that upon initial insertion of clothing and user input, the washing machine will automatically carry out the hydrating, soaking, agitation, and drying stages of the wash cycle.

## Slide 5: Integral Background Information: Design Criteria & Constraints
Specific challenges this design must address:
Must operate independently of gravity
Cannot produce excessive vibrations
Must fit given size requirements
Must be energy efficient & compatible with the ship
All wash water must be recoverable for purification
Can operate without the use of detergents or additives to wash water
Can operate with minimal water usage (500 mL)
Must be able to carry out all phases of the wash cycle or be compatible with additional machinery to complete the wash cycle
Must be compatible with ISS electric grid and utilities

## Slide 6: Integral Background Information: The Basic Wash Cycle
The Wash Cycle:
Initial User Input: Not a part of the physical wash process. Clothing item is inserted, and the wash method and duration is determined
Hydration Phase: Where clothing is soaked with clean water
Soaking: An intermediary phase, clothing is left to soak as water disperses throughout the clothing item. Can occur before and/or after the agitation process.
Agitation Phase: Clothing-water mixture has mechanical energy applied to it to dislodge and evacuate contaminants, with water being a medium that
Drying Phase: Where wash water is removed from clothing item to be purified and reused
Disinfecting Phase: Through any number of means, bacteria is sterilized on clothing item to prevent the cultivation and spread of pathogens.
Product and Byproduct Retrieval: Not a part of the physical wash process. The wash cycle has concluded. Clothing is made to be retrievable by the user, and all byproducts are outputted appropriately

## Slide 7: Key ideas of Press Displacement Washing Machine:
Basic Function:
Clothing is compressed in a cylindrical wash chamber by a piston head. The movement of the piston head compressing the clothing displaces the fluid in the chamber. This accomplishes two main objectives:
Compresses the clothing item and generating a flow of fluid through the clothing item for agitation
Displacing fluids such as air and water so that the hydrating and drying phases can be preformed alongside other functions integral to the wash process

## Slide 8: Key ideas of Press Displacement Washing Machine:
Fluid Flow:
The piston performs multiple functions While the primary purpose of the mechanism behind the washing machine is performing the wash process on a piece of clothing, it also physically moves the fluid for each function, so no other components
The piston head acting on the clothing is essentially a piston in a reciprocating pump. Fluid is pumped in and out of the wash chamber by the piston. Unlike a typical reciprocating pump, the fluid displaced is sent to a reservoir, which is the space created by the space left above the piston when it extends. The fluid displaced is then pushed again by the piston head back from the reservoir to the wash chamber.
Much like a reciprocating pump, as long as flow is not inhibited, the pressure of the fluid remains constant. While a lot of force is used to compress the clothing

## Slide 9: Internal Plumbing and Components Explained
Valve (Generic): Controls flow by either opening or closing off a fluid connection in a pipe
Check Valve: Only allows fluid flow in one direction
Stop-Check Valve: Can open or close, but only allows flow in one direction while open
Filter or Strainer: filters contaminants from fluid

## Slide 10
Chamber Top
Pipe to Reservoir
Reservoir
Acting Piston
Wash Chamber
Pipe to Wash Chamber
Access Hatch

## Slide 11: Key ideas of Press Displacement Washing Machine:

## Slide 12: Basic Wash Cycle: Hydration Phase

## Slide 13: Specific Wash Plan
Water Soluble Contaminants and Liquids:
Non-Soluble Solids:
Non-Soluble Liquids:

## Slide 14: Advantages of design
Design is fully capable of working in microgravity environments
Air and water are kept completely separate throughout the entire wash process, simplifying design and operation
The machine has variable chamber size while being rigid and robust, allowing for accommodation of multiple clothing types and sizes without additional work or parts
Simple mechanism reduces risk of jamming and allows for easy maintenance
Basic function is adaptable: auxiliary components can be easily added for additional functionality

## Slide 15: Criteria and Constraints Explained: Challenges Presented by Microgravity Environments
Definition of a Microgravity Environment
A microgravity environment is a place where the constant of gravity is less than that of Earth’s. The effects of microgravity is felt in outer space or orbit, where gravity is effectively zero, but it is also felt on the Moon and Mars, where gravity is less than that or Earth’s.
Containing Fluids
On Earth, a glass would hold water in it as long as it is held upright. In space, where gravity is not present, the same glass would not be able to contain the water, as the fluid would just float from the opening at the top of the glass. Additionally, removing fluids from reservoirs cannot be done using gravity. Because of these facts, containers need to be completely sealed to prevent fluid leakage. Additionally, draining a tank of water is rather challenging without gravity to push it out for you.
Keeping Air and Water Separate
On earth, separating materials in a fluid mixture is often done using gravity. With the constant of gravity, more dense objects and fluids tend to sink while less dense objects and fluids tend to float. Examples of this would be oil or a boat floating on water, or a balloon rising in the air. In space with a sealed rigid container, fluids such as water and air do not fully separate there is no up or down for them to float or sink to. Because of this, fluids tends to mix in a way that makes retrieving one or another other from a reservoir difficult to do without additional mechanisms, and makes manipulating fluids more challenging in some ways.
Surface Tension
Surface tension is an attraction of molecules in a fluid towards each other. This attraction forms a mass with an easily distinguishable surface. This is why drops of water tend to be spherical and you can fill a glass of water just over the rim. On earth, the effects of surface tension are usually so small, the effects of gravity masks its presence. In microgravity environments however, surface tension is much more prevalent. Without the presence of gravity, water molecules will adhere to each other, and form rounded volumes. These volumes will stick to and cover surfaces. This makes draining water from reservoirs with water and complex surfaces challenging to do effectively.

## Slide 16: Criteria and Constraints Explained: Challenges Presented by Microgravity Environments Cont.
Because of the issues listed, there are some design considerations that need to be made including but not limited to:
Containers and hydraulic systems must be fully sealed from the atmosphere and other systems to prevent leakage and contamination of fluids within the system
Fluid must be forcefully drained, as there are no forces acting on them that will do so otherwise like gravity
If a container has fluid added or removed from it, the container either has to change shape or have a new fluid added or removed from the container to account for this change in volume
Air and water need to be isolated from each other at all times during the wash process to mitigate water loss and ensure proper operation
If air and water are allowed in the same container at one time, these fluids must be separated to be reclaimed. measures must be taken to account for surface tension and mixing of these fluids

## Slide 17: Criteria and Constraints Explained: The Challenges of Space Ship Compatibility Explained
Size: The larger and heavier an object is, the harder it is to get it into orbit. Because of this, space ships are relatively small, meaning everything that is needed for passengers and cargo has to be too. For this prototype, it needs to be able to fit into an ISS Double Locker on an Express Rack.
Limited Water Availability: Water is heavy and takes up a lot of space, and to get a large amount into orbit is challenging. Though water can be reclaimed, water cannot be made or sourced from anywhere else onboard a ship. Because of this, as little water as possible is taken into space, so it has to be used sparingly. Additionally, losing this water due to a failure of the machine is possible, so as little water as possible should be used to mitigate potential loss. For one clothing item only 500 mL of water can be used.
Water Reusability: Since water cannot be made on a space ship, it has to be purified and recycled. Because of this, all water used for washing clothing has to be recoverable for purification. This means any additives or treatments that damage the water reclamation system such as detergents cannot be used.
Power Efficiency: With limited ways of sustainably producing power for a space ship power consumption is also kept to a minimum. Because of this, no heating or cooling devices can be used as the primary function driving the wash process. Additionally, all components must be electronically operated, and be compatible with the space ship power grid.
Limit Vibrations: Space ships do not travel while touching a medium that will absorb any movement or forces acting on them like a boat or car, and they are made to be as light as possible. As a result, Vibrating forces have a pronounced effect on space ships. A space ship can have resonant frequencies, where an oscillating force matches the reaction forces of the ship, causing it to vibrate more and more. For this reason vibrations and oscillating forces have to be eliminated on machinery attached to the ship.

## Slide 18: Criteria and Constraints Explained: Additional Info
Why Just Wash One Clothing Item at a Time?
On a space ship, there’s no outside that contaminants can enter the ship from. Additionally, clothing makes less skin contact in space. Because of this, clothing and actually gets dirty at a slower rate than on earth. In this way, the ability to clean large loads of laundry is not particularly important. Additionally, failure of machinery can result in a loss of water and damage of plant components. In order to limit potential losses, less water is used, and thus, less clothing can be washed. This design can be adjusted to accommodate a larger load with more load if needed.
Why Skip the Disinfection Phase of the Wash Process?
Disinfection phase of the wash process is skipped because the purpose of this design is to solve the issue of physically manipulating clothing in order to remove contaminants and clean. Disinfection, while important for washing clothing, requires little significant hardware, and can be added to the design as an auxiliary component.

## Slide 19: Design Spaces to Explore

## Slide 20: Unsolved Issues of Design